- neighborhood radius
- motion probability
- immigration probability
- birth rate
- death rate
- virus morbidity
- vectored infection probability
- contact infection probability
- spontaneous infection probability
- recovery probability
- re-susceptible probability

Neighborhood radius This parameter determines the size of the interaction
neighborhood that a cell interrogates for state information.
The motion radius defines the greatest distance, measured in cells, a host can move during a
time step. The infection radius defines the greatest distance the virus pathogen can travel outside the body of a host on its own.

Motion probability The individuals in the world are permitted to move between cells. The motion probability determines the frequency of this motion. For example, if
the motion probability, p move , is set to 0.4, you would expect roughly two in five
hosts to shift from the cell they currently reside in to another cell within its motion neighborhood.

Vectored infection rate The actual probability of spread, p vectored , is a function of the vectored
infection parameter provided by the user, p input , and the density of susceptible
hosts in the local interaction neighborhood.

P.vectored = susceptible pop./neighborhood capacity * P.input

Cell update algorithm
The cell update function takes as arguments all the parameters outlined in the previous section along with the state information from the cells in the interaction neighborhood of the cell in question.
The cell update algorithm is performed in two phases: the movement phase and the infection phase. It is important to note that the effects of the movement phase are instantaneous, that is, cell populations are immediately updated to reflect host traversals. During the infection phase, although implemented sequentially over the lattice, each cell evolves synchronously with all the others.

Movement phase
1. Select a random cell from the world.
2. For each of the individuals in the cell, randomly select a neighboring cell
and move the individual into it. This movement is dependent on the motion
probability parameter described earlier and the destination cell not being
full.
3. Repeat from step one until all the cells in the world have been accounted
for.

Infection and recovery phase The ordering of events during the infection
and recovery phase are such that similar operations are performed consecutively,
that is, all operations affecting host population are dealt with before infections
are calculated. Other inter-leavings should be tried in order to examine possible
biases.

- Select the first cell.
- Deduct the ‘natural deaths’ from the cell population.
- Deduct the deaths from virus morbidity.
- Add to the population any newborns.
- Add any immigrant population.
- Compute inter-cell (vectored) infections.
- Compute intra-cell (contact) infections.
- Compute spontaneous infections.
- Compute host recoveries.
- Compute re-susceptibles.
- Repeat from step one for the next cell until all cells have been accounted for.

This model does not take into account other parameters such as the latency
or incubation times illustrated in Figure 2. Latency is the lag between being infected and becoming infective, and incubation is the delay between being infected
and becoming symptomatic. These times could be implemented by introducing
another state, for example ‘E’ for exposed hosts, who are infected but not infective

Corridors of Spread
Towns and roads are human constructed features that
attract high population densities. Conversely, the scenario could be depicting
non-cultural features, for example, rivers that promote development along their
shores or mountain ranges that limit settlement and population movement. Their
key attribute is their directed and linear shape rather than a wide uniform population density.